## Slide 1: Unit 3: Source Coding
Shannon-Fano coding, Huffman Coding, Run length coding, LZW algorithm
Prepared by
G.Balamurugan
Assistant Professor,
Electronics Department, MIT

## Slide 2: Need for compression
Uncompressed data can take up a lot of space, which is not good for limited hard drive space and internet download speeds.
While hardware gets better and cheaper, algorithms to reduce data size also helps technology evolve.
One minute of uncompressed HD video can be over 1GB. How can we fit a two hour film on a 25GB blueray disc?
Speech compression
Image compression: JPEG

## Slide 3: Compression
Process of reducing the size of a data is referred to as data compression.
Compression advantage
  Reduce size of data
  Reduce bandwidth
  Reduce latency
  Reduce storage needed
  Reduce transmission cost

## Slide 4: Types of compression
Lossless compression
Lossless compression compresses the data in such a way that, when data is decompressed it is exactly the same as it was before compression i.e. there is no loss of data.
Lossless algorithms are used to compress text files and numeric data
2. Lossy compression
Lossy compression is the one that does not promise that the data received is exactly the same as data send i.e. the data may be lost. This is because a lossy algorithm removes information that it cannot later restore.
Lossy algorithms are used to compress still images, video and audio.
Notes: Lossy Compression:
Human perception
  Less sensitive to some information
  Can discard less important data

## Slide 5: Classification of codes
Symbol | Code 1 | Code 2 | Code 3 | Code 4 | Code 5 | Code 6
X1 | 00 | 00 | 0 | 0 | 0 | 1
X2 | 01 | 01 | 1 | 10 | 01 | 01
X3 | 00 | 10 | 00 | 110 | 011 | 001
X4 | 11 | 11 | 11 | 111 | 0111 | 0001
A source encoded the symbols in binary codes with symbol 0 and 1.
A code is a set of vectors called code words.
1. Fixed length codes: A fixed length code is one whose codeword length is fixed.
Code 1 and Code 2 – Fixed length codes
2. Variable length codes: A variable length code is one whose codeword length is not fixed.
Except Code 1 and Code 2 – Variable length codes
3. Distinct codes: A code is distinct if each code word is distinguishable from other codes.
Except Code 1 – Distinct codes

## Slide 6: Classification of codes
Symbol | Code 1 | Code 2 | Code 3 | Code 4 | Code 5 | Code 6
X1 | 00 | 00 | 0 | 0 | 0 | 1
X2 | 01 | 01 | 1 | 10 | 01 | 01
X3 | 00 | 10 | 00 | 110 | 011 | 001
X4 | 11 | 11 | 11 | 111 | 0111 | 0001
4. Prefix-free codes: A prefix code is one in which no code word forms prefix of another code word. Such codes are also called Instantaneous codes.
Code 2, 4 and 6 – Prefix free codes
5. Uniquely Decodable codes: A distinct code is uniquely decodable, if the original source sequence can be reconstructed perfectly from the encoded sequence.
Code 3 – Not a uniquely decodable
Code 2,4 and 6 – prefix free codes – uniquely decodable
Code 5 – does not satisfy prefix free condition - but it is uniquely decodable

## Slide 7: 1. Fixed Length Coding

## Slide 8: 1. Fixed Length coding
Assume we wish to represent the 26 letters (A-Z) using bits.
Require 5 bits to represent a character
= 32 ( Codewords )
Each of the letters can be uniquely decodable using 5 bits.
The fixed length code for the English alphabet (ASCII)
Character | ASCII | Codeword
A | 65 | 01000001
B | 66 | 01000010
C | 67 | 01000011
D | 68 | 01000100
E | 69 | 01000101

## Slide 9: 2. Shannon-Fano coding
Technique:
  Use variable length codes based on frequency of occurrence

## Slide 10: 2. Shannon-Fano coding
List the source symbols in order of decreasing probability.
Partition the set into two sets that are as close to equiprobable as possible, and assign 0 to the upper set and 1 to the lower set.
Continue this process, each time partitioning the sets with as nearly equal probabilities as possible until further partitioning not possible.
Algorithm steps:

## Slide 11: Problem 1
Consider a six symbol alphabet where the probability of each symbol is tabulated below
Using Shannon-Fano coding find the codeword for each symbol and find the efficiency of the code.
Symbol | Probability of occurrence
A | 0.30
B | 0.25
C | 0.20
D | 0.12
E | 0.08
F | 0.05

## Slide 12: Problem 1 (contd.)
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 |  |  |  |  | 
B | 0.25 |  |  |  |  | 
C | 0.20 |  |  |  |  | 
D | 0.12 |  |  |  |  | 
E | 0.08 |  |  |  |  | 
F | 0.05 |  |  |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 |  |  |  |  | 
B | 0.25 |  |  |  |  | 
C | 0.20 |  |  |  |  | 
D | 0.12 |  |  |  |  | 
E | 0.08 |  |  |  |  | 
F | 0.05 |  |  |  |  | 
0.55
0.45
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 |  |  |  | 
B | 0.25 | 0 |  |  |  | 
C | 0.20 | 1 |  |  |  | 
D | 0.12 | 1 |  |  |  | 
E | 0.08 | 1 |  |  |  | 
F | 0.05 | 1 |  |  |  | 
0.30
0.25
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 |  |  | 
B | 0.25 | 0 | 1 |  |  | 
C | 0.20 | 1 |  |  |  | 
D | 0.12 | 1 |  |  |  | 
E | 0.08 | 1 |  |  |  | 
F | 0.05 | 1 |  |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 |  |  |  | 
D | 0.12 | 1 |  |  |  | 
E | 0.08 | 1 |  |  |  | 
F | 0.05 | 1 |  |  |  | 
0.20
0.25
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 |  |  | 
D | 0.12 | 1 | 1 |  |  | 
E | 0.08 | 1 | 1 |  |  | 
F | 0.05 | 1 | 1 |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 |  |  | 
E | 0.08 | 1 | 1 |  |  | 
F | 0.05 | 1 | 1 |  |  | 
0.12
0.13
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 |  |  | 
E | 0.08 | 1 | 1 |  |  | 
F | 0.05 | 1 | 1 |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 | 0 |  | 
E | 0.08 | 1 | 1 | 1 |  | 
F | 0.05 | 1 | 1 | 1 |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 | 0 | - | 110
E | 0.08 | 1 | 1 | 1 |  | 
F | 0.05 | 1 | 1 | 1 |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 | 0 | - | 110
E | 0.08 | 1 | 1 | 1 | 0 | 
F | 0.05 | 1 | 1 | 1 | 1 | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Stage 4 | Codeword
A | 0.30 | 0 | 0 | - | - | 00
B | 0.25 | 0 | 1 | - | - | 01
C | 0.20 | 1 | 0 | - | - | 10
D | 0.12 | 1 | 1 | 0 | - | 110
E | 0.08 | 1 | 1 | 1 | 0 | 1110
F | 0.05 | 1 | 1 | 1 | 1 | 1111
Shannon Compressed binary value : 0100110. Find the transmitted characters
Transmitted characters : BAD
H(x)=2.36 bits/symbol
L=2.38 bits/symbol
Efficiency:
Entropy of source:
Average Length of the code

## Slide 13: Problem 2
A DMS X has five equally likely symbols
  (a) Construct a Shannon-Fano code for X, and calculate the efficiency of the code.
  (b) Construct another Shannon-Fano code and compare the results.
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Codeword
A | 0.20 |  |  |  | 
B | 0.20 |  |  |  | 
C | 0.20 |  |  |  | 
D | 0.20 |  |  |  | 
E | 0.20 |  |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Codeword
A | 0.20 | 0 | 0 | - | 00
B | 0.20 | 0 | 1 | - | 01
C | 0.20 | 1 | 0 | - | 10
D | 0.20 | 1 | 1 | 0 | 110
E | 0.20 | 1 | 1 | 1 | 111
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Codeword
A | 0.20 |  |  |  | 
B | 0.20 |  |  |  | 
C | 0.20 |  |  |  | 
D | 0.20 |  |  |  | 
E | 0.20 |  |  |  | 
Symbol | P(x) | Stage 1 | Stage 2 | Stage 3 | Codeword
A | 0.20 | 0 | 0 | - | 00
B | 0.20 | 0 | 1 | 0 | 010
C | 0.20 | 0 | 1 | 1 | 011
D | 0.20 | 1 | 0 | - | 10
E | 0.20 | 1 | 1 | - | 11
(a)
(b)
H(x)=2.32 bits/sym
L=2.4 bits/sym
H(x)=2.32 bits/sym
L=2.4 bits/sym

## Slide 14: 3. Huffman Coding
Technique:
  Use variable length codes based on frequency of occurrence

## Slide 15: 3. Huffman Coding
Proposed by Dr. David A. Huffman in 1952
  “A Method for the Construction of Minimum Redundancy Codes”
Applicable to many forms of data transmission
  Our example: text files
Huffman codes can be used to compress information
The basic idea is that instead of storing each character in a file as an 8-bit ASCII value, we will instead store the more frequently occurring characters using fewer bits and less frequently occurring characters using more bits
  On average this should decrease the filesize (usually ½)
Principle
  Use fewer bits to represent frequent symbols
  Use more bits to represent infrequent symbols

## Slide 16: Huffman Coding
List the source symbols in order of decreasing probability.
Combine the probabilities of the two symbols having the lowest probabilities, and reorder the resultant probabilities: this step is called reduction 1. The same procedure is repeated until there are two ordered probabilities remaining.
Start encoding with the last reduction, which consists of exactly two ordered probabilities. Assign 0 as the first digit in the code words for all the source symbols associated with the first probability; assign 1 to the second probability.
Now go back and assign 0 and 1 to the second digit for the two probabilities that were combined in the previous reduction step, retaining all assignments made in step 3.
Keep regressing this away until the first column is reached.
Algorithm steps:

## Slide 17: Problem 1
A source emits independent sequence of symbols from a source alphabet containing 5 symbols with probabilities 0.4, 0.2, 0.2, 0.1 and 0.1. Calculate Huffman code word for the source moving a combined symbol as low as possible and coding efficiency.
Message
Probability
0.4
0.2
0.2
0.1
0.1
Stage-1
Stage-2
Stage-3
0.4
0.2
0.2
0.2
0.4
0.4
0.2
0.6
0.4
(0)
(1)
(0)
(1)
(0)
(1)
(0)
(1)
Symbol | Probability | Codeword
X1 | 0.4 | 1
X2 | 0.2 | 01
X3 | 0.2 | 000
X4 | 0.1 | 0010
X5 | 0.1 | 0011

## Slide 18: Problem 1 (Contd.)
Efficiency:
Entropy of source:
Average Length of the code
H(x)=2.12 bits/sym
L=2.2 bits/sym
Symbol | Probability | Codeword
X1 | 0.4 | 1
X2 | 0.2 | 01
X3 | 0.2 | 000
X4 | 0.1 | 0010
X5 | 0.1 | 0011

## Slide 19: Problem 2
In the message , each letter occurs the following percentage of times:
Compute Huffman code for this source, moving a combined symbol as high as possible and calculate the efficiency of the code.
Letter | A | B | C | D | E | F
% of occurrence | 23 | 20 | 11 | 9 | 15 | 22
Solution:
Letter | A | B | C | D | E | F
Probability | 0.23 | 0.20 | 0.11 | 0.09 | 0.15 | 0.22
Message
Probability
0.23
0.22
0.20
0.15
0.11
0.09
Stage-1
Stage-2
Stage-3
Stage-4
0.23
0.22
0.20
0.20
0.15
0.35
0.23
0.22
0.20
0.42
0.35
0.23
0.58
0.42
(0)
(1)
(0)
(1)
(0)
(1)
(0)
(1)
(0)
(1)
Letter | A | B | C | D | E | F
Codeword | 01 | 000 | 110 | 111 | 001 | 10

## Slide 20: Problem 2 (contd.)
Letter | A | B | C | D | E | F
Codeword | 01 | 000 | 110 | 111 | 001 | 10
Efficiency:
Entropy of source:
Average Length of the code
H(x)=2.505 bits/sym
L=2.55 bits/sym
Note: Combine the probabilities of the two symbols having the lowest probabilities and reorder the resultant probabilities:
Either if reorder by moving a combined symbol as low as possible or moving a combined symbol as high as possible it never affects the entropy and efficiency of the source.
Only codeword changes for each symbol. ( Check it for problem 2)

## Slide 21: Problem 3
Consider a DMS with alphabet {S0,S1,S2} and statistics {0.4,0.35,0.25} for its output. (i) Determine Huffman code for this source and find the efficiency (ii)Determine Huffman code for this source taking two symbols at a time and find the efficiency
Symbol | Probability | Codeword
X1 | 0.4 | 1
X2 | 0.35 | 00
X3 | 0.25 | 01
H(x)=1.5589 bits/sym
L=1.60 bits/sym
Symbol | X3Probability | Codeword
X1X1 |  | 
X1X2 |  | 
X1X3 |  | 
X2X1 |  | 
X2X2 |  | 
X2X3 |  | 
X3X1 |  | 
X3X2 |  | 
X3X3 |  | 
Symbol | X3Probability | Codeword
X1X1 | 0.16 | 
X1X2 | 0.14 | 
X1X3 | 0.1 | 
X2X1 | 0.14 | 
X2X2 | 0.1225 | 
X2X3 | 0.0875 | 
X3X1 | 0.1 | 
X3X2 | 0.0875 | 
X3X3 | 0.0625 | 
Symbol | X3Probability | Codeword
X1X1 | 0.16 | 10
X1X2 | 0.14 | 001
X1X3 | 0.1 | 111
X2X1 | 0.14 | 010
X2X2 | 0.1225 | 011
X2X3 | 0.0875 | 0001
X3X1 | 0.1 | 0000
X3X2 | 0.0875 | 1100
X3X3 | 0.0625 | 1101
H(x)=1.5589 bits/sym
L=3.1775 bits/sym
Inference:
Thus grouping two letters has improved the coding efficiency
Common pairs : th, sh, de, ng, te, es, re, he, at
Entropy Property:
H(xx)=H(x^2) = 2H(x)

## Slide 22: 4. Run Length Encoding
  Technique: Find & compress repetitive sequences

## Slide 23: 4. Run Length Encoding
Used to reduce the size of a repeating string of characters.
Repeating string is called run.
RLE cannot achieve high compression ratios compared to other compression methods.
But it is easy to implement and is quick to execute.
Run length encoding – TIFF, JPG, BMP and fax machines.
RLE contains : a count and a symbol

## Slide 24: Problem 1
Consider the following bit stream
S= 11111111111111100000000000000000001111
Compress the above string by using Run length encoding and find the compression ratio. Assume the codeword length is 5.
Solution:
There are (15,1) (19,0) and (4,1).
Codeword length : 5 (a count + a symbol)
(15,1) (15,0) (4,0) (4,1)
Encode bit stream : 11111 11110 01000 01001
Compression ratio : 20:38 (1:1.9)

## Slide 25: 5. Lempel-Ziv Welch (LZW)
(Dictionary based coding)
Technique:
  Build pattern dictionary
  Replace patterns with index into dictionary

## Slide 26: Lempel-Ziv Welch (LZW)
LZW algorithm is one of many algorithms used for compression. It is typically used to compress certain image files. It is lossless, meaning no data is lost when compressing.
IDEA: rely on reoccurring patterns to save data space.
Typically every character is stored with 8 binary bits, allowing up to 256 unique symbols for the data. (ASCII)
This algorithm tries to extend this library to 9 to 12 bits per character. The new unique symbols are made up of combinations of symbols that occurred previously in the string.

## Slide 27: Problem 1
Compress the string : “thisisthe”
Uncompressed ASCII:
116 104 105 115 105 115 116 104 101
We require 72bits.

## Slide 28
Start adding pairs of symbols to dictionary of words. When we reach a pair that we have already placed in the dictionary replace that pair with our new dictionary value.
For this tiny string we will only need 9 bits allowing up to 512 unique symbols.

## Slide 29
Compress the string : “thisisthe”
Compressed string “thisisthe” : 116 104 105 115 258 256 101
Our symbols are now made upto 9bits each instead of 8.
The number of bits is : 9*7=63bits
(63/72)=87.5% of what it is used to be.
Each symbol use 9bits, 512 unique characters
Imagine how much larger the file could be before we need to use 11bits, 12 or 13 bits
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
i (105) | s (115) |  | 
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
i (105) | s (115) |  | 
is (258) | t (116) | is(258) | ist (260)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
i (105) | s (115) |  | 
is (258) | t (116) | is(258) | ist (260)
t (116) | h (104) |  | 
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
i (105) | s (115) |  | 
is (258) | t (116) | is(258) | ist (260)
t (116) | h (104) |  | 
th (256) | e (101) | th (256) | the (261)
Current | Next | Output | Add to dictionary
t (116) | h (104) | t (116) | th (256)
h (104) | i (105) | h (104) | hi (257)
i (105) | s (115) | i (105) | is (258)
s (115) | i (105) | s (115) | si (259)
i (105) | s (115) |  | 
is (258) | t (116) | is(258) | ist (260)
t (116) | h (104) |  | 
th (256) | e (101) | th (256) | the (261)
e (101) | - | e (101) | 
‘’Is” is in the dictionary. Check if “ist” is ?
‘’th” is in the dictionary. Check if “the” is ?
Notes: Thisisastring – Does the compression works?

## Slide 30: LZW Uncompressing
To uncompress, we do need to know how many bits were used in the compression, the one new information that is kept with the data when saved to a file ( else, the number of bits is specified by a program or a user).
We can read in the characters and builds the new dictionary the same way as we did for compressing.
When we reach a symbol outside the ASCII range (>255), then we should have that value ready to be seen in the dictionary.

## Slide 31: Decompress LZW
The compressed value 116 104 105 115 258 256 101
Current | Next | Output | Add to dictionary
116 | 104 | 116 | 116 104 (256)
104 | 105 | 104 | 104 105 (257)
105 | 115 | 105 | 105 115 (258)
115 | 258 | 115 | 115 105 (259)
258 | 256 | 258 | 105 115 116 (260)
256 | 101 | 256 | 116 104 101(261)
101 | - | 101 | -
Output : 116 104 105 115 258 256 101
Decompressed characters : t h i s is th e
Inference:
If we used 8 bits (ASCII) to represent the given string : 9x8=72bits
If we used LZW (9bits) to represent the given string: 7x9=63bits
Compression ration between ASCII and LZW : 1: 0.875